| BIROTEHNA d.o.o. Smederevo Karađorđeva 21; 11300 Smederevo Laboratorija za etaloniranje Calibration laboratory Smederevo, ul. Đure Salaja 28, tel: 026/ 640-333 fax: 026/462-11-11 E-mail: office@birotehna.com Web sajt: http://www.birotehna.com |  |
| --- | --- |
| Uverenje o etaloniranju Calibration Certificate |

| Predmet etaloniranja: | Elektromehanička vaga sa neautomatskim funkcionisanjem |
| --- | --- |
| Object | Electronical non automatic weighing instrument |
| Proizvođač: |  |
| Manufacturer |  |
| Tip: |  |
| Type |  |
| Serijski broj: |  |
| Serial number |  |
| Podnosilac zahteva: Customer |  |
| Uverenje broj: |  |
| Calibration certificate No: |  |
| Broj stranica uverenja: |  |
| Number of pages of the certificate |  |
| Datum etaloniranja: |  |
| Date of calibration |  |

Bez odobrenja laboratorije uverenje o etaloniranju sme se umnožavati isključivo kao celina. Uverenje o etaloniranju bez potpisa i pečata nije važeće. This calibration certificate may not be reproduced other than in full. Calibration certificates without signature and seal are not valid.

| Merenje izvršio | Datum | Pečat | Tehnički rukovodilac laboratorije |
| --- | --- | --- | --- |
| Person in charge | Date | Seal | Head of the calibration laboratory |

| 1. Predmet etaloniranja / Calibration Object |  |
| --- | --- |
|  | Tip: / Type |  |
|  | Proizvođač: / Manufacturer |  |
|  | Serijski broj: / Serial number |  |
|  | Temperaturni koeficijent TC: / Temperature coefficient TC |  |
|  | Opseg merenja: / Weighing range |  |
|  | Podeljak d: / Scale interval d |  |

| 2. Tegovi / Weights |
| --- |
|  | Garnitura tegova: / Set of weights |  |
|  | Serijski broj: / Serial number |  |
|  | Uverenje o etaloniranju: / Calibration certificate |  |
|  | Pojedinačni tegovi: / Weights |  |
|  | Serijski broj: / Serial number |  |
|  | Uverenje o etaloniranju: / Calibration certificate |  |

3. Postupak etaloniranja / Calibration procedure

Etaloniranje je izvršeno prema dokumentu Guidelines on the Calibration of Non – Automatic weighing instruments, EURAMET cg-18 v4.0 (11/2015), koji se odnosi na etaloniranje elektromehaničkih vaga sa neautomatskim funkcionisanjem. Etaloniranje obuhvata: The calibration was done according to document Guidelines on the Calibration of Non – Automatic weighing instruments, EURAMETcg -18 v4.0 (11/2015). The calibration comprised:

- Određivanje vrednosti ponovljivosti / Repeatability

- Određivanje vrednosti odstupanja / Deviation of indication

- Određivanje vrednosti ekscentričnosti / Eccentricity

| 4. Mesto etaloniranja / Calibration site |  |
| --- | --- |
| Mesto gde je vaga postavljena / Laboratorija: |  |
| Site of the weighing instrument / Laboratory No. |  |
| 5. Uslovi merenja / Measuring conditions |
| Promena temperature na mestu upotrebe: Temperature variation on site | (tambijent = (C |
| Nepovoljno strujanje vazduha / Strong draught |  | Da / Yes | X | Ne / No |
| Nepovoljne vibracije / Strong vibrations |  | Da / Yes | X | Ne / No |
| Vaga prethodno podešena / Initial adjustment |  | Da / Yes | X | Ne / No |

| Promena temperatura tokom etaloniranja: Temperature variations during calibration | t = () (C |
| --- | --- |

### Temperatura u toku etaloniranja izmerena je etaloniranim termometrom TESTO AG; testo 905-T2;  serijski broj: 39814698009, uverenje: 19420t3569 - Laboratorija d.o.o. Beograd

The temperature during the calibration have been measured with a calibrated thermometer

6. Rezultati merenja / Measuring results

6.1. Rezultati merenja pre podešavanja / Measuring results before the adjustment

Na predmetu etaloniranja NISU izvršena podešavanja / The calibration subject has not been adjusted

6.2. Rezultati merenja nakon podešavanja (ili rezultati ukoliko podešavanje nije izvršeno) / Measuring results after the adjustment of the calibration subject (or the results if the adjustment has not been performed)

Određivanje vrednosti ponovljivosti / Repeatability

| Opterećenje Test load |  |
| --- | --- |
|  | očitanja / readings |
| 1 |  | g |
| 2 |  | g |
| 3 |  | g |
| 4 |  | g |
| 5 |  | g |
| 6 |  | g |

| Eksperimentalna standardna devijacija: | S = |
| --- | --- |
| The experimental standard deviation is |  |

Određivanje vrednosti odstupanja pokazivanja / Deviation of indication

| Merenje broj Measuring No. | Opterećenje Test load | Odstupanje (E) Deviation of indication (E) |
| --- | --- | --- |
| 1 |  | g |  | g |
| 2 |  | g |  | g |
| 3 |  | g |  | g |
| 4 |  | g |  | g |
| 5 |  | g |  | g |

Određivanje vrednosti ekscentričnosti / Eccentricity

| Opterećenje Test load |  |
| --- | --- |
| Položaj Load position | Odstupanje u odnosu na centar (0) Deviation of indication referring to centre |
| 1 |  | g |
| 2 |  | g |
| 3 |  | g |
| 4 |  | g |

Dobijene vrednosti odgovaraju trenutnom stanju vage u trenutku etaloniranja. The values stated apply for the condition of the weighing instrument at the time of calibration.

7. Merna nesigurnost / Measurement uncertainty

7.1. Merna nesigurnost pre podešavanja / Measurement uncertainty before the adjustment

Na predmetu etaloniranja nisu izvršena nikakva podešavanja On the subject of the calibration no adjustments have been made

7.2. Merna nesigurnost nakon podešavanja (ili nesigurnost ukoliko nije izvršeno podešavanje) / Measurement uncertainty after the adjustment (or the uncertainty if no adjustment have been made)

Merna nesigurnost vage u tačkama etaloniranja: Measurement uncertainty of weighing instrument in calibration points

Pokazivanje: Indication: kp U(E) Merna nesigurnost rezultata izražena je kao proširena merna nesigurnost koja je dobijena množenjem kombinovane merne nesigurnosti faktorom obuhvata kp koji za normalnu raspodelu odgovara nivou poverenja od približno 95 %. Merna nesigurnost je izračunata u skladu sa dokumentom Evaluation of the Uncertainty of Measurement in Calibration, EA-4/02 M. Reported is the expanded uncertainty witch results from the standard uncertainty by multiplication with coverage factor kp.The value of the measure and is found within the attributed interval with a probability of approximately 95%. It has been evaluated according to document Evaluation of the Uncertainty of Measurement in Calibration, EA-4/02 M. 8. Sledivost rezultata merenja / Traceability Rezultat etaloniranja je slediv do nacionalnog etalona, koji predstavlja realizaciju jedinice mase u skladu sa Međunarodnim sistemom mernih jedinica (SI). Korišćeni etalon u tački 2. ovog Uverenja. This calibration certificate documents the traceability to national standards, which realize the units of mass according to the International System of Units (SI). Complete list of used reference weights is given in chapter 2. of this Certificate. 9. Etaloniranjem je određena merna nesigurnost vage sa neautomatskim funkcionisanjem. Sve korekcije i njihove merne nesigurnosti, koje su rezultat razlike gustine materijala predmeta koji se meri na vagi i gustine tega za podešavanje treba da odredi korisnik. Measurement uncertainty of non automatic weighing instrument is evaluated by calibration. All corrections and their measurement uncertainties, that are result of difference between density of the body that is measured on non automatic weighing instrument and density of weight of adjustment, must be determinated by the user. 10. Odstupanja u odnosu na specificirane uslove/ Specified conditions deviations U slučaju odstupanja predmeta etaloniranja od specificiranih uslova, koji su pismenim putem prihvaćeni od strane korisnika usluga, Laboratorija ne snosi odgovornost za odstupanja u rezultatima dobijenim u procesu etaloniranja tog predmeta. In case of deviations of the calibration subject to the specified conditions, which have written acceptance by the customer, Laboratory denies the responsibility for the deviations of the results occured during the calibration procedure of the subject.

Dodatak Uverenja o etaloniranju*

Addition of a Calibration Certificate*

Izmereni rezultati W  u upotrebi / Weighing results in use

Pod normalnim uslovima upotrebe, koji uključuju:

- promenu temperature na mestu upotrebe vage u okviru (  (C;

- da se mereni predmet  ne mora spuštati tačno u centar prijemnika operećenja (tasa);

- ostvarivanje očitanja R sa ili bez upotrebe tare (neto ili bruto vrednosti);

- da se merenje  vrši u opterećivanju;

- nepodešavanja vage;

- neizvršenje korekcije očitanih rezultata merenja, R.

Under normal conditions of use, including

- room temperature varying within ± 5(C;

- loads applied without special care to apply centre of gravity in centre of load

receptor;

- obtaining readings R with or without tare balancing (Net or Gross values):

- measurement in increasing steps;

- not to adjusting the instrument;

- not applying any correction to the readings R.

izmereni rezultat W je / Weighing result W is

W = R ( Ugl (W) =

gde je Ugl (W) ukupna proširena merna nesigurnost, koja iznosi: / Ugl (W) is global measurement uncertainty

Ugl (W) =

Ukupna merna nesigurnost rezultata izražena je kao proširena merna nesigurnost koja je dobijena množenjem kombinovane merne nesigurnosti faktorom obuhvata k=2 koji za normalnu raspodelu odgovara nivou poverenja od približno 95 %. Merna nesigurnost je izračunata u skladu sa dokumentom Evaluation of the Uncertainty of Measurement in Calibration, EA-4/02 M.

Reported is the global  expanded uncertainty wich results from the standard uncertainty by multiplication with coverage factor k=2.The value of the measurand is found within the attributed interval with a probability of approximately 95%. It has been evaluated according to document Evaluation of the Uncertainty of Measurement in Calibration, EA-4/02 M.

Kraj  uverenja  o etaloniranju.

End of a calibration certificate.

_______________________________________________________________________________________

* - Dodatak uverenja o etaloniranju nije pod znakom akreditacije !

Addition of a calibration certificate is not under accreditation sign !

# Text boxes

4                    1

3                     2

0

4

3

1

2

0

4

1

2

3